## Slide 1: eduroam series
Installation and Configuration of eduroam server and FLR

## Slide 2: Introduction
Derrick Ssemanda
Systems and Software Engineer
Research and Education Network for Uganda (RENU)
Email
  dssemanda@renu.ac.ug
  systems@renu.ac.ug

## Slide 3: About this presentation
Installing and configuration of eduroam server and Federation Level Radius (FLR)
Brief introduction to some concepts.
All of them as technical as possible
All in relatively easy and relatable terms
Sorry – It has less politics
Also included; Proposed consideration for an African CTLR

## Slide 4: eduroam
Basic introduction
Outline
Introduction
Terminology
General
eduroam - technically
Comparison with other technologies

## Slide 6: eduroam
SSID with the name ‘eduroam’ (Fully lower case)
WPA2-Enterprise
Authentication with help of RADIUS
Group of RADIUS and Proxy servers working together
Each RADIUS server handles at least 1 realm/domain
Username in the format user@realm
  For example; systems@renu.ac.ug, user - systems, realm - renu.ac.ug

## Slide 7: Terminologies
Definitions of some terms
Outline
APs
IMS
IdP
SP
Proxy
FLR
TLR

## Slide 8: Access Points ( APs)
Provides users with access to resources
Uses local or external authentication
For external authentication, it sends out an Access-Request based on the credentials provided
It sends it out to the RADIUS server(SP) and waits for an Access-Accept or a Access-Reject

## Slide 9: Examples
Ubiquiti
TP-Link
Cambium
D-Link
MikroTik
Linksys

## Slide 10: Service Provider ( SP )
RADIUS server
Forwards requests from APs to other RADIUS servers(IdP or FLR)
As well as returning Access-Accept/Aeject back to the AP
Examples include; FreeRADIUS3, daloRADIUS

## Slide 11: Identity Provider ( IdP )
Sometimes referred to as home_server
Receives requests from other RADIUS or proxy servers
Checks and authenticates the user in the request using a user database(IMS) it is configured to connect to
Returns Access-Accept/Reject

## Slide 12: Identity Management System ( IMS )
Fancy title
Sometimes referred to as Identity Management (IDM)
One or set of tools which manage user life cycle
Can range from text files, excel documents all the way to Active Directory/Directory service
IdP authenticates users by checking from any IMS its configured to connect to
Another term: Identity and Access Management (IAM)

## Slide 13: Examples
Text files
Excel Sheet
SQL Databases
FreeIPA
Windows Active Directory
Source: https://wxbcyber.com/user-lifecycle-management.php

## Slide 14: eduroam - proxying
Local authentications handled by server
External authentications are proxied out to their home server
Connections in between involve proxy server
These servers include FLR and TLR

## Slide 15: Federation Level Radius ( FLR )
Federation Level RADIUS
Responsible for at least one top-level domain
  E.g. *.ug for Uganda
Connects eduroam servers together

## Slide 16: Confederation top-level RADIUS server ( TLR )
Confederation top-level RADIUS server
Connects FLRs together

## Slide 17: eduroam - Technically

## Slide 18: eduroam - Technically
Mobile devices save a connection profile for each SSID
Research networks agreed to use an SSID “eduroam”
This SSID is similar across the globe and uses WPA2-Enterprise
The mobile device will connect to SSID in the same way as always when it detects using the saved profile
A network of RADIUS servers ensures that the same profile works by proxying it back to the home IdP which authenticates the device

## Slide 19: Comparison with other technologies

## Slide 20: Comparison with Network
L3 Network
RADIUS network

## Slide 21: Comparison with DNS
DNS
RADIUS

## Slide 22: eduroam
Deployment with FreeRADIUS3
Outline
Introduction
Structure
Deployment
Testing and Troubleshooting

## Slide 23: Introduction - freeRADIUS
Most popular RADIUS server
Opensource
Scalable
Feature rich
Supports virtual sites

## Slide 24: Structure
Similar to Apache2
Mods-enabled symlink used modules from mods-enabled
Same applies to sites
Accepts connections from NAS mentioned in clients.conf
Proxies requests according to the proxy.conf

## Slide 25: Structure – Core config files
radiusd.conf
Clients.conf
Proxy.conf
sites-enabled/*
mods-enabled/*

## Slide 26: Structure – radiusd.conf
Reading freeRADIUS configs starts here
Defines the configuration parameters for the server
Includes references to all other config files

## Slide 27: Structure – clients.conf
APs which connect to the RADIUS are added here
Defines necessary information to configure a RADIUS client (AP)

## Slide 28: Structure – proxy.conf
RADIUS proxies are mentioned here
In a similar way, decisions on which proxy server to send a request from a realm is also specifies here

## Slide 29: Structure – proxy.conf Cont’d
Proxy servers are defined as ‘home_server’
And they forward to realms/domains as per the configuration

## Slide 30: Structure – sites-enabled/
Stores virtual sites
These symlink to sites-available
eduroam is configured here, as well as eduroam-inner-tunnel

## Slide 31: Structure – sites-enabled/virtual-site
Defines a server.
Within the server, it defines the subsections
Then places mods within a subsection
In each subsection, the modules are run in order

## Slide 32: Structure – mods-enabled/*
Files symlink to mods-available
Contains modules used by the virtual site
Each module is made up of a module name and can contain either zero or more variables definitions
Modules are loaded into a virtual site by listing them in a subsection

## Slide 33: Structure – mods-enabled/module
A module is built from rlm_module
Files here are enabled files containing variables for the modules
Each file normally contains variables for one module
Notes: This should give an explanation to as why you still have to install freeradius-ldap

## Slide 34: Deployment - Requirements
Ubuntu 18 server with access to the internet

## Slide 35: Deployment
Clone git: https://github.com/RENUUG/eduroamIdP
Copy paste template, clients, secrets and inventory
Edit radius_flr.yml
Run script
Notes: Doesn't have other DBs yet

## Slide 36: Demo

## Slide 37: Walk Through
Notes: What we have done

## Slide 38: Troubleshooting Tips
Check and confirm that indentation is okay
Run the command “freeradius –X”
  This informs you where the errors are arising from

## Slide 39: FLR server
Deployment with radsecproxy
Outline
Introduction
Structure
Deployment
Testing

## Slide 40: Introduction
Generic RADIUS proxy
Flexible
Small
Efficient
Easy to configure
Supports both IPv4 and IPv6

## Slide 41: Structure
Basically has one initial config file
Default location: /usr/local/etc/radsecproxy.conf
Other files can be added by including them in this file
Installation comes with radsecproxy-hash which prints hash of Ethernet MAC addresses

## Slide 42: Structure – radsecproxy.conf
Proxy server checks this file when the service is started. Returns error if not found
Can include other files
Ignores whitespace
Comments using #
Uses a block structure as shown below
client newone{
some_commands here
}

## Slide 43: Deployment – Pre-installation
On an Ubuntu 18 server, upgrade all packages
Install software packages that will help in compiling radsecproxy
  apt install build-essential libssl-dev nettle-bin nettle-dev wget

## Slide 44: Deployment - Installation
Download latest version (https://radsecproxy.github.io/)
Unzip and change directory to the new folder created
Make installations from source files using
  ./configure ; make ; make check; make install
Create radsecproxy.conf file – [template attached]
Create system unit files – [template attached]
Enable it to start on start up
Notes: Supposed to be on different lines but don’t have space

## Slide 45: Deployment - Configuration
Edit radsecproxy.conf
Add or remove content
Restart radsecproxy

## Slide 46: Demo

## Slide 47: African TLR
Considerations for an African CTLR
Proposed diagram
Software to be used
Advantages

## Slide 48: Diagram

## Slide 49: Software Used
Radsecproxy
Haproxy – Load balancing
Ansible
Rsync
All open source

## Slide 50: Advantages of this model
No single point of failure
Load balancing can easily be implemented
Set up costs are easily distributed
Another step at African collaboration
Notes: African NRENS can still eduroam without the need for external
Can also remain operation in case of anything happening to the top level RADIUS servers

## Slide 51: Conclusion

## Slide 52: REFERENCES
https://wiki.geant.org/display/H2eduroam/freeradius-sp
https://wiki.geant.org/pages/viewpage.action?pageId=121346324
https://radsecproxy.github.io/radsecproxy.conf.html

## Slide 53: THE END
Thank you for your time